## Slide 1: An Optimized 3D-Stacked Memory Architecture by Exploiting Excessive, High-Density TSV Bandwidth
Dong Hyuk Woo
Nak Hee Seong
Dean L. Lewis
Hsien-Hsin S. Lee
Electrical and Computer Engineering
Georgia Tech
The 16th International Symposium on High-Performance Computer Architecture

## Slide 2: 3D Integration
Multiple layers
  Homogeneous tech.
  Heterogeneous tech.

## Slide 3: F2F Via and Through Silicon Via (TSV)
Short, fast, and dense
Face-to-Back
(Scalable)
Face-to-Face
(limited to
2 die tiers)
4um pitch in 2011 (ITRS 2007)
Can enlarge device area

## Slide 4: 3D-Stacked DRAM
Higher
bus clock
Cache line-wide bus
Multiple channels
64B = 512 TSVs
per channel

## Slide 5
Are we exploiting
its full potential?

## Slide 6: Von Neumann Bottleneck-Aware Design
Cache
capacity
Cache
line size
Issue
width
Load
scheduling
Prefetching
Multi-threading
Minimize
off-chip traffic!!!

## Slide 7: Revisiting Cache Line Size
Chart: 429.mcf
| 64 | 128 | 256 | 512 | 1024 | 2048 | 4096
32KB | 10.8658 | 6.4261 | 4.2105 | 3.8505 | 12.2013 | 28.4467 | 27.2403
64KB | 10.7107 | 6.2581 | 3.9196 | 2.7125 | 3.182 | 8.6882 | 25.8743
128KB | 10.6326 | 6.1812 | 3.8221 | 2.5172 | 1.8097 | 1.5169 | 5.9337
256KB | 10.5833 | 6.1378 | 3.7747 | 2.4535 | 1.6742 | 1.1826 | 1.0141
512KB | 10.5437 | 6.1064 | 3.7462 | 2.4217 | 1.6293 | 1.1185 | 0.7965
1MB | 10.5056 | 6.0764 | 3.7218 | 2.4001 | 1.6063 | 1.0916 | 0.7491
2MB | 9.8467 | 5.7793 | 3.5825 | 2.3299 | 1.567 | 1.0665 | 0.726
4MB | 7.0382 | 4.6177 | 3.1436 | 2.168 | 1.502 | 1.0361 | 0.707
8MB | 5.7052 | 3.7087 | 2.5865 | 1.8787 | 1.3692 | 0.9771 | 0.6781
8MB
w/ 64B lines
256KB
w/ 4KB lines
Cache pollution

## Slide 8: SMART-3D
3D memory interface design to allow page-level fetching
  No more trailing-edge effect
    Lots of TSVs
  Overhead of pollution much eliminated
    Practically no more contention

## Slide 9: Issues of a Naïve Cache Design
Look up a 4KB line in an 8-way 1MB$.
64B lines
2^12 bit lines
2^11 word lines
4KB lines
2^18 bit lines
2^5 word lines
64x
1/64x
Almost linear increase in access latency!
64x

## Slide 10: SMART-3D: Separate Fill / WB Network
Read / write
from L1$
64B access
Common event
Fill / write-back
from/to DRAM
4KB access
Rare event
Let’s separate them!

## Slide 11: Conventional Subarray Technique
subarray
mat
Cache controller
64B read / write
request from L1$
64B fill / write-back traffic
64B TSVs
64B
32B
16B
subbank

## Slide 12: SMART-3D Cache Design

## Slide 13: SMART-3D Cache Design
64 subbanks
(4KB/64B=64)
64B read / write
request from L1$

## Slide 14: SMART-3D Cache Design
4KB fill / write-back traffic
(64B per subbank)
One or two cycles higher latency

## Slide 15: SMART-3D System Architecture
Face-to-Face
Face-to-Back
Processor layer
Memory
controller
layer
N layers
of DRAM
One L2 subbank
One subbank of MSHR and write-back buffer

## Slide 16: DRAM Design Issues in SMART-3D
256Mb DRAM array
per tile
256 TSVs
per tile
128 array (= one bank)
lookup per row buffer miss
256Mb array
2KB row buffer
256 TSVs

## Slide 17: DRAM Design Issues in SMART-3D
256Mb DRAM array
per tile
256 TSVs
per tile
32k Shared TSVs
Two array (= one bank)
lookup per row buffer miss

## Slide 18: DRAM Design Issues in SMART-3D
256Mb DRAM array
per tile
32k Shared TSVs
Folded DRAM layers
256 TSVs
per tile

## Slide 19: Simulation Framework
SESC simulator + Modified Cacti
42 applications from SPEC2006int, SPEC2006fp, Olden, NU-MineBench
3GHz, 4-wide, 14-stage OoO processor
IL1
  2-way, 64B line, 32KB, 1-cycle latency
DL1
  2-way, 64B line, 32KB, 2-cycle latency

## Slide 20: Experimental Configurations
2D-Base
L2$: 8-way, 64B line, 1MB, 6-cycle
DRAM: 8B-wide, 12.8 GBps bus, 350-cycle
2D-GHB
2D-VLS
3D-Base
3D-GHB
SMART-3D
2D-Base + Global History Buffer prefetcher
2D-Base + Virtual Line Scheme w/o software control
Same L2$ as 2D-Base
3D-Base + GHB
L2$: 8-way, (4KB line), 1MB, 7-cycle
DRAM: 4KB-wide, 250-cycle
DRAM: 64B-wide, 250-cycle

## Slide 21: Single Core Results
Chart: Speedup
| 429. mcf | 462. libquantum | 471. omnetpp | 473. astar | 483. xalancbmk | 410. bwaves | 433. milc | 436. cactusADM | 437. leslie3d | 450. soplex | 459. GemsFDTD | 482. sphinx3 | Geomean (MI)
2D-GHB | 0.99947 | 2.7963 | 1.0449 | 1.161 | 1.0331 | 1.2534 | 1.3559 | 1.4616 | 1.9127 | 2.2547 | 1.7692 | 2.2442 | 1.3983
2D-VLS | 1.1534 | 5.5682 | 0.2131 | 0.2916 | 0.73545 | 1.8052 | 0.74939 | 0.044005 | 1.7795 | 1.6609 | 0.59246 | 2.8906 | 0.81705
3D Base | 1.2788 | 1.3402 | 1.1059 | 1.146 | 1.3177 | 1.4039 | 1.391 | 1.1765 | 1.237 | 1.3784 | 1.265 | 1.2884 | 1.2449
3D-GHB | 1.277 | 3.7791 | 1.2152 | 1.2919 | 1.3569 | 1.8814 | 1.9566 | 1.607 | 2.0467 | 3.0528 | 2.0576 | 2.6606 | 1.6862
SMART-3D | 2.808 | 5.8811 | 1.3259 | 1.1017 | 2.2013 | 3.1354 | 3.5147 | 0.86385 | 2.2035 | 4.9549 | 2.1432 | 3.8351 | 2.1431
Perfect L2 | 3.3404 | 6.7319 | 1.8692 | 1.7054 | 5.4302 | 3.259 | 6.5592 | 1.7604 | 2.274 | 6.0242 | 2.8903 | 4.2182 | 2.8249
1.40x
0.82x
1.25x
1.69x
2.14x
2.83x
Bad spatial locality

## Slide 22: Dual-Core Results
Chart: Speedup
| 410 459 | 410 462 | 410 473 | 429 450 | 429 473 | 433 437 | 433 450 | 436 450 | 436 462 | 436 483 | 437 483 | 450 482 | 459 462 | 462 473 | 462 482 | 462 483 | Geo mean
3D-GHB (4MB) | 2.1886 | 2.2267 | 1.6406 | 1.7906 | 1.3393 | 1.74 | 1.6226 | 1.4895 | 1.8339 | 1.6747 | 1.8943 | 1.9308 | 2.7961 | 2.2506 | 3.0108 | 2.8965 | 1.9657
SMART-3D (1MB) | 2.6822 | 3.4331 | 2.2333 | 1.997 | 1.3446 | 2.2368 | 2.5699 | 1.134 | 1.8286 | 0.91039 | 1.853 | 2.6847 | 3.4833 | 3.245 | 4.6112 | 4.1104 | 2.3058
SMART-3D (2MB) | 2.7152 | 3.3996 | 2.2245 | 2.2021 | 1.4369 | 2.2538 | 2.7598 | 1.2785 | 1.8629 | 1.0251 | 1.9337 | 2.9366 | 3.4952 | 3.2363 | 4.602 | 4.2243 | 2.4025
Perfect L2 | 2.8444 | 3.7623 | 2.3786 | 3.3007 | 1.835 | 2.9441 | 4.3961 | 2.1676 | 2.65 | 1.9805 | 2.4128 | 3.7229 | 3.8327 | 3.643 | 5.1796 | 5.5944 | 3.1245
Baseline: 2D-Base (2MB)
1.96x
2.31x
2.40x
3.12x

## Slide 23: Energy Trade-Off
+ L2 read / write energy
+ L2 fill / WB energy
+ Bus fill / WB energy
- DRAM lookup energy

## Slide 24: Why do we save energy in DRAM?
Conventional
3D DRAM
Row Buffer
Hit rate ~ 50%
Capacity << L2$
One cache line
0x0000 0000
0x0000 0040
0x1000 0000
0x1000 0040
0x0000 0080
0x0000 00c0

## Slide 25: Why do we save energy in DRAM?
DRAM
for
SMART-3D
0x0000 0000
0x0000 0040
0x1000 0000
0x1000 0040
0x0000 0080
0x0000 00c0
One cache line
L2 Hits

## Slide 26: Energy Result
Chart: 462.libquantum
| 3D-Base | SMART-3D
L2 Read | 0.019541 | 0.020681
L2 Write | 0.0046713 | 0.0054618
L2 Fill | 0.018977 | 0.00094568
L2 Write-back | 0.00481 | 0.00031024
TSVs for DRAM bus | 0.0036096 | 0.0036252
Wires on a DRAM layer | 0.028041 | 0.028162
DRAM array lookup | 0.92035 | 0.094441

## Slide 27: Energy Result
Chart: 436.cactusADM
| 3D-Base | SMART-3D
L2 Read | 0.007312 | 0.022629
L2 Write | 0.0014215 | 0.006584
L2 Fill | 0.0045716 | 0.036033
L2 Write-back | 0.0013739 | 0.016145
TSVs for DRAM bus | 0.00090144 | 0.14808
Wires on a DRAM layer | 0.0070028 | 1.1503
DRAM array lookup | 0.97742 | 3.4772
On average, 47%
4.79

## Slide 28: Conclusion

## Slide 29: Conclusion
Page fetching through HD-TSVs
3D cache fill / write-back network
Energy-efficient 3D DRAM design
More than 2x speedup
Simultaneously saving energy

## Slide 30: Questions?
Georgia Tech
MARS
http://arch.ece.gatech.edu

## Slide 31: False Sharing
Same in the L1 bus (64B)
May have an issue in multi-socket platforms
L2 Cache
Bank 0
L2 Cache
Bank 1
Memory
Controller 0
Memory
Controller 1
On-chip Interconnection
Core 0
Core 1
Core 2
Core 3
L2 Cache
Bank 0
L2 Cache
Bank 1
Memory
Controller 2
Memory
Controller 3
On-chip Interconnection
Core 4
Core 5
Core 6
Core 7
Off-chip
Interconnection
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM

## Slide 32: Adaptive SMART-3D
  Similar to Sector Cache
Fetch 64B if
  The target page is mapped to the remote memory space.
  Any of the target page is cached in the remote L2$
    Page-level Bloom filter similar to RegionScout or Page Sharing Table
Details of miss handling is in the paper.

## Slide 33: Multi-Core
Chart: Speedup
| 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | barnes | cholesky | fft | fmm | lu | ocean
2D Base (nMB) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3D Base (nMB) | 1.0166 | 1.0164 | 1.0108 | 1.0898 | 1.0689 | 1.0501 | 1.1497 | 1.1739 | 1.191 | 1.0192 | 1.0193 | 1.0195 | 1.0499 | 1.0502 | 1.0532 | 1.3199 | 1.34 | 1.3691
SMART-3D (nMB) | 1.0243 | 1.0337 | 1.0211 | 1.3648 | 1.2568 | 1.1775 | 1.2098 | 1.2971 | 1.6768 | 1.0089 | 1.015 | 1.022 | 1.1489 | 1.1513 | 1.1628 | 3.6017 | 4.5409 | 6.4864
Perfect L2 | 1.056 | 1.0535 | 1.0344 | 1.3809 | 1.2674 | 1.1825 | 1.6439 | 1.8667 | 2.1417 | 1.0584 | 1.059 | 1.0597 | 1.1519 | 1.1554 | 1.1664 | 3.8511 | 4.7555 | 6.6288
Chart: Speedup
| 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | 2C | 4C | 8C | radiosity | radix | raytrace | volrend | water-n2 | water-sp | Geomean
2D Base (nMB) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3D Base (nMB) | 1.0007 | 1.001 | 1.0009 | 1.2297 | 1.2271 | 1.2995 | 1.0143 | 1.0062 | 1.0064 | 1.1068 | 1.1492 | 1.1892 | 1.0008 | 1.001 | 1.0012 | 1.007 | 1.0016 | 1.0022 | 1.0795 | 1.0831 | 1.0929
SMART-3D (nMB) | 1.002 | 1.0026 | 1.003 | 2.7288 | 2.718 | 3.0526 | 1.01 | 1.0098 | 1.0076 | 1.2758 | 1.4087 | 1.5669 | 0.92265 | 0.99474 | 1.0003 | 1.0204 | 1.0045 | 1.0063 | 1.3006 | 1.3437 | 1.434
Perfect L2 | 1.0021 | 1.0029 | 1.0032 | 2.7961 | 2.7804 | 3.1338 | 1.0504 | 1.023 | 1.0231 | 1.2916 | 1.4188 | 1.5784 | 1.0027 | 1.0035 | 1.0043 | 1.0227 | 1.0049 | 1.0066 | 1.3704 | 1.405 | 1.4797

## Slide 34: Multi-Socket
Chart: 
| barnes | cholesky | fft | fmm | lu | ocean | radiosity | radix | raytrace | volrend | water-n2 | water-sp | Geomean
2D Base (1MB each) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
3D Base (1MB each) | 1.0134 | 1.0787 | 1.1281 | 1.0184 | 1.0452 | 1 | 1.0007 | 1 | 1.0144 | 1.0832 | 1.031 | 1.0057 | 1.0342
SMART-3D (1MB each) | 0.94266 | 1.4429 | 1.4086 | 0.97519 | 1.2521 | 3.6287 | 0.95769 | 1.5999 | 0.80162 | 1.3032 | 0.94713 | 0.97549 | 1.2347
Perfect L2 | 1.0774 | 1.6774 | 2.0427 | 1.0982 | 1.2638 | 4.3048 | 1.009 | 3.0063 | 1.1194 | 1.4656 | 1.3101 | 1.0385 | 1.5177